## Slide 1: Synthesis of a Forklift Controller

## Slide 2: The Forklift

## Slide 3: Sensors of Forklift
Two distance sensors
  for walls
  for cargo and low obstacles
Color sensor to detect station
Emergency off button

## Slide 4: Requirements (obligations of forklift)
Do not run into obstacles.
  Pay special attention to low obstacles.
Only pick up or drop cargo at stations.
Do not attempt to lift cargo if cargo is lifted.
Always keep on delivering cargo.
Never drop cargo at the station where it was picked up.
Stop moving if emergency off switch is pressed.

## Slide 5: Assumptions
The forklift will always be able to eventually find a station with cargo by going forward. The same applies for delivering cargo.
The forklift will always be able to eventually leave a station by going forward or backward.
The forklift can back up or turn to avoid obstacles.
// If the forklift stops at a station it remains there.

## Slide 6: C&C Model of Forklift

## Slide 7: C&C Model of Forklift
ForkLift
«Deploy»
StationSensor(S1) stationSense
LiftMotor(A) mLift
Controller
MontiArcAutomaton
DistanceSensor(S2, 20) distSense
DistanceSensor(S4, 9) cargoSense
Button(S3) emgOffButton
Motor(C) mRight
Motor(B) mLeft

## Slide 8: Controller and Datatypes
«enumeration» MotorCmd
FWD BWD STOP
«enumeration» LiftCmd
LIFT DROP NIL
«enumeration» Distance
CLEAR
BLOCKED
Controller
boolean atStation
Distance obstacle
Distance cargo
MotorCmd lMot
MotorCmd rMot
LiftCmd lift
boolean emgOff
boolean liftAck

## Slide 9: Wrappers and Computation
Integration of hardware wrappers and computation parts requires
  component definition with no implementation
  implementation in Java of
    compute() method
    optional: constructor, init(), and setup()
  framework will do composition

## Slide 10: Wrapper: StationSensor
StationSensor(SensorPort sp)
boolean atStation
public StationSensorImpl(SensorPort sp) {
sensor = new ColorSensor(sp);
sensor.setFloodlight(Color.BLUE);
}
public void compute() {
if (sensor.getRawLightValue() < 400) {
sense.setCurrentValue(true);
} else {
sense.setCurrentValue(false);
}
}

## Slide 11: Wrapper: DistanceSensor
DistanceSensor(SensorPort sp, int cm)
Distance sense
public DistanceSensorImpl(SensorPort sp, int cm) {
this.cm = cm;
sensor = new UltrasonicSensor(sp);
sensor.continuous();
}
public void init() {compute();};
public void compute() {
if (sensor.getDistance() < cm) {
sense.setCurrentValue(Distance.BLOCKED);
} else {
sense.setCurrentValue(Distance.CLEAR);
}
}

## Slide 12: Wrapper: LiftMotor
public LiftMotorImpl(MotorPort mp) {
motor = new NXTRegulatedMotor(mp);
motor.setAcceleration(1000);
motor.resetTachoCount();
}
public void compute() {
if (cmd.getNextValue() != null) {
switch (cmd.getNextValue()) {
case DROP:
motor.rotateTo(0, true);
break;
case LIFT:
motor.rotateTo(600, true);
break;
case NIL:
break;
}
}
LiftMotor(MotorPort mp)
LiftCmd cmd
boolean liftAck
boolean atDonePos = true;
try {
atDonePos = !motor.isMoving() && (motor.getTachoCount() == 0 || motor.getTachoCount() == 600);
} catch (Exception e) {
e.printStackTrace();
}
if (working && atDonePos) {
ack.setCurrentValue(true);
working = false;
} else {
ack.setCurrentValue(false);
}
}

## Slide 13: Wrapper: Motor
public MotorImpl(MotorPort mp) {
motor = new NXTRegulatedMotor(mp);
motor.setAcceleration(1000);
motor.resetTachoCount();
}
public void compute() {
if (cmd.getNextValue() != null) {
switch (cmd.getNextValue()) {
case STOP:
motor.stop();
break;
case BWD:
motor.rotate(-180, true);
break;
case FWD:
motor.rotate(180, true);
break;
}
}
}
Motor(MotorPort mp)
MotorCmd cmd

## Slide 14: Scheduling Execution
ForkLift
«Deploy»
StationSensor(S1) stationSense
LiftMotor(A) mLift
Controller
MontiArcAutomaton
DistanceSensor(S2, 20) distSense
DistanceSensor(S4, 9) cargoSense
Button(S3) emgOffButton
Motor(C) mRight
Motor(B) mLeft
1
2
3
4
5
6
7
8

## Slide 15: Scheduler in CMP Format
<<Deploy>>component ForkLift {
// exception to put it first because it sends data to controller
component LiftMotor(lejos.nxt.Motor.A) mLift;
// sensors
component StationSensor(lejos.nxt.SensorPort.S1) stationSense;
component DistanceSensor(lejos.nxt.SensorPort.S2, 20) distSense;
component Button(lejos.nxt.SensorPort.S3) emgOffButton;
component DistanceSensor(lejos.nxt.SensorPort.S4, 9) cargoSense;
// controller
component Controller controller;
// actuators
component Motor(lejos.nxt.Motor.B) mLeft;
component Motor(lejos.nxt.Motor.C) mRight;
// input from sensors to controller
connect stationSense.sense -> controller.station;
connect distSense.sense -> controller.sense;
connect emgOffButton.pressed -> controller.emgOff;
connect cargoSense.sense -> controller.cargo;
connect mLift.ack -> controller.liftAck;
// output from controller to actuators
connect controller.lift -> mLift.cmd;
connect controller.mLeft -> mLeft.cmd;
connect controller.mRight -> mRight.cmd;
}

## Slide 16: Synthesis Specification

## Slide 17: “Interface” Definition
VARENV
ext cargo : { CLEAR, BLOCKED };
ext sense : { CLEAR, BLOCKED };
ext station : boolean;
ext emgOff : boolean;
VAR
ext mLeft : { FWD, STOP, BWD, XXX };
ext mRight : { FWD, STOP, BWD, XXX };
ext lift : { LIFT, DROP, NIL, XXX };

## Slide 18: Some Abbreviations for Specification
DEFINE
backing := mLeft = BWD & mRight = BWD;
stopping := mLeft = STOP & mRight = STOP;
turning := mLeft = BWD & mRight = FWD;
forwarding := mLeft = FWD & mRight = FWD;
dropping := lift = DROP;
lifting := lift = LIFT;
lowObstacle := (cargo = BLOCKED & station = 0);

## Slide 19: Some Guarantees
Do not run into obstacles.
[] ((sense = BLOCKED | lowObstacle) -> ! forwarding);
Only pick up or drop cargo at stations.
[] (!station -> lift = NIL);
Always keep on delivering cargo.
[] <> ((lift = DROP) | emgOff | lowObstacle);

## Slide 20: Some Assumptions
The forklift will always be able to eventually leave a station by going forward.
[] ((forwarding) -> <> (!station | stopping));
The forklift will always be able to eventually find a station with cargo by going forward.
[] ((forwarding & !spec_loaded) -> <> ((station & cargo = BLOCKED) | backing | stopping));

## Slide 21: Synthesized Controller
state S0, S1, S2, S3, S4, S5, S6[initial], S7, S8, S9, S10, S11;
S0 -> S7 {cargo:CLEAR, sense:CLEAR, station:0, emgOff:0} / {mLeft:FWD, mRight:FWD, lift:NIL};
S0 -> S11 {cargo:BLOCKED, sense:BLOCKED, station:0, emgOff:1} / {mLeft:STOP, mRight:STOP, lift:NIL};
S0 -> S10 {cargo:BLOCKED, sense:CLEAR, station:1, emgOff:1} / {mLeft:STOP, mRight:STOP, lift:NIL};
S0 -> S11 {cargo:CLEAR, sense:CLEAR, station:0, emgOff:1} / {mLeft:STOP, mRight:STOP, lift:NIL};
S0 -> S7 {cargo:CLEAR, sense:BLOCKED, station:0, emgOff:0} / {mLeft:BWD, mRight:FWD, lift:NIL};
S0 -> S7 {cargo:CLEAR, sense:CLEAR, station:1, emgOff:0} / {mLeft:FWD, mRight:FWD, lift:NIL};
S0 -> S11 {cargo:CLEAR, sense:BLOCKED, station:0, emgOff:1} / {mLeft:STOP, mRight:STOP, lift:NIL};
S0 -> S10 {cargo:CLEAR, sense:CLEAR, station:1, emgOff:1} / {mLeft:STOP, mRight:STOP, lift:NIL};
S0 -> S10 {cargo:BLOCKED, sense:BLOCKED, station:1, emgOff:1} / {mLeft:STOP, mRight:STOP, lift:NIL};
S0 -> S7 {cargo:CLEAR, sense:BLOCKED, station:1, emgOff:0} / {mLeft:BWD, mRight:FWD, lift:NIL};
S0 -> S10 {cargo:CLEAR, sense:BLOCKED, station:1, emgOff:1} / {mLeft:STOP, mRight:STOP, lift:NIL};
S0 -> S0 {cargo:BLOCKED, sense:CLEAR, station:0, emgOff:0} / {mLeft:BWD, mRight:BWD, lift:NIL};
S0 -> S7 {cargo:BLOCKED, sense:CLEAR, station:1, emgOff:0} / {mLeft:BWD, mRight:BWD, lift:NIL};
S0 -> S7 {cargo:BLOCKED, sense:BLOCKED, station:1, emgOff:0} / {mLeft:BWD, mRight:BWD, lift:NIL};
S0 -> S11 {cargo:BLOCKED, sense:CLEAR, station:0, emgOff:1} / {mLeft:STOP, mRight:STOP, lift:NIL};
S0 -> S0 {cargo:BLOCKED, sense:BLOCKED, station:0, emgOff:0} / {mLeft:BWD, mRight:BWD, lift:NIL};
S1 -> S1 {cargo:CLEAR, sense:CLEAR, station:0, emgOff:0} / {mLeft:FWD, mRight:FWD, lift:NIL};
S1 -> S6 {cargo:BLOCKED, sense:BLOCKED, station:0, emgOff:1} / {mLeft:STOP, mRight:STOP, lift:NIL};
S1 -> S5 {cargo:BLOCKED, sense:BLOCKED, station:1, emgOff:0} / {mLeft:STOP, mRight:STOP, lift:LIFT};
S1 -> S8 {cargo:BLOCKED, sense:CLEAR, station:1, emgOff:1} / {mLeft:STOP, mRight:STOP, lift:NIL};
S1 -> S6 {cargo:CLEAR, sense:CLEAR, station:0, emgOff:1} / {mLeft:STOP, mRight:STOP, lift:NIL};
S1 -> S1 {cargo:CLEAR, sense:BLOCKED, station:0, emgOff:0} / {mLeft:BWD, mRight:FWD, lift:NIL};
S1 -> S1 {cargo:CLEAR, sense:CLEAR, station:1, emgOff:0} / {mLeft:FWD, mRight:FWD, lift:NIL};
S1 -> S8 {cargo:BLOCKED, sense:BLOCKED, station:1, emgOff:1} / {mLeft:STOP, mRight:STOP, lift:NIL};
S1 -> S6 {cargo:CLEAR, sense:BLOCKED, station:0, emgOff:1} / {mLeft:STOP, mRight:STOP, lift:NIL};
S1 -> S8 {cargo:CLEAR, sense:CLEAR, station:1, emgOff:1} / {mLeft:STOP, mRight:STOP, lift:NIL};
S1 -> S1 {cargo:CLEAR, sense:BLOCKED, station:1, emgOff:0} / {mLeft:BWD, mRight:FWD, lift:NIL};
...

## Slide 22: Generated Java Code
switch (this.state) {
case S0:
if (this.cargo.getCurrentValue() != null
&& this.cargo.getCurrentValue() == Distance.CLEAR
&& this.sense.getCurrentValue() != null
&& this.sense.getCurrentValue() == Distance.BLOCKED
&& this.station.getCurrentValue() != null
&& this.station.getCurrentValue() == true
&& this.emgOff.getCurrentValue() != null
&& this.emgOff.getCurrentValue() == false) {
this.state = State.S6;
this.mLeft.setNextValue(MotorCmd.BWD);
this.mRight.setNextValue(MotorCmd.FWD);
this.lift.setNextValue(LiftCmd.NIL);
}
if (this.cargo.getCurrentValue() != null
&& this.cargo.getCurrentValue() == Distance.CLEAR
&& this.sense.getCurrentValue() != null
&& this.sense.getCurrentValue() == Distance.BLOCKED
&& this.station.getCurrentValue() != null
&& this.station.getCurrentValue() == true
&& this.emgOff.getCurrentValue() != null
&& this.emgOff.getCurrentValue() == true) {
this.state = State.S0;
this.mLeft.setNextValue(MotorCmd.STOP);
this.mRight.setNextValue(MotorCmd.STOP);
this.lift.setNextValue(LiftCmd.NIL);
}
...

## Slide 23: The Running System

## Slide 24: C&C Model of Forklift
ForkLift
«Deploy»
StationSensor(S1) stationSense
LiftMotor(A) mLift
Controller
MontiArcAutomaton
DistanceSensor(S2, 20) distSense
DistanceSensor(S4, 9) cargoSense
Button(S3) emgOffButton
Motor(C) mRight
Motor(B) mLeft